## Slide 1: CUDA Tutorial Matrix-Matrix Multiply
Ryan Bergmann
2/4/2014

## Slide 2: CUDA and GPUs in a Nutshell
Shared memory machine with large SIMD lanes
SIMD execution abstracted by threads and thread blocks
Coalesced reads/writes necessary for full performance
Has a user-programmable cache that can help with data reuse (you’ll see later)
CUDA adds minimal extensions to C/C++ (and Fortran)

## Slide 3: Shared Memory, as a Paradigm
Threads share the same memory space
  Problems in this kitchen with many cooks?
  Fighting for finite resources
    32-64 32bit registers per SM limits active threads/blocks
  Collisions
    Data is read by multiple threads but isn’t broadcast to all threads
  Data races
    Multiple threads reading and writing to the same address
    Incrementing an event count, for example

## Slide 4: SIMD
Single Instruction Multiple Data
Amortize control overhead over SIMD width
Kitchen – one cook opens fridge, 4 cooks get different things out to cut up
Both from Wikimedia Commons

## Slide 5: SIMD
Hex-core CPU
  6 cores, 2 issue, 4-way SIMD, 3.46GHz
448 ‘CUDA cores’
  14 cores, 2 issue, 16-way SIMD, 1.54GHz
GPUs get a LOT of their power from SIMD
  Must use it for good performance… or at least try to use it as much as possible

## Slide 6: Coalesced Reads/Writes
Memory subsystems are SIMD-like as well
Must coalesce in order to use full memory bandwidth
http://www.cmsoft.com.br/tutorialOpenCL/OptimizIcoalescDiagram.png

## Slide 7: Host Thread
Host computer must launch GPU kernel
  Kernel is a serial program performed by all threads
Data must be copied from host to card
  “Zero-copy” memory now available, hides copy commands
Once the kernel completes, control is returned to the host
  Asynchronous calls possible
New hardware can launch kernels from kernels
  Host must still initialize launches
CUDA C Programming Guide, NVIDIA Co.

## Slide 8: Threads, Blocks, and Grids
Many, many threads
  Execute same serial code
Organized in blocks
  Threads in a block cooperate
Blocks make up the grid
Each thread and block have a unique ID
Blocks execute in an arbitrary order
CUDA C Programming Guide, NVIDIA Co.

## Slide 9: Launching a Kernel From the Host
kernel <<< grid_dimensions , block_dimensions >>> (arguments);
kernel = the name of the kernel
grid_dimensions = dim3(x,y,z) number of blocks in the (x,y,z) dimensions
block_dimensions = dim3(x,y,z) number of threads in the (x,y,z) dimensions within a block
arguments = input values, pointers to arrays, etc.

## Slide 10: A Kernel
Predefined local values
  Used for thread identification and indexing
__global__
  GPU kernel to be launched from the host
__device__
  GPU function to be used within a kernel
__device__ float d_add(float a, float b){
return a+b;
}
__global__ void kernel( unsigned len, float* a){
// get thread index
int row = blockIdx.y * blockDim.y + threadIdx.y;
int col = blockIdx.x * blockDim.x + threadIdx.x;
//return if over the length
if(row>=len | col>=len){return;}
// do something…
a[row*len + col] = d_add(1,2);
}

## Slide 11: Shared Memory, as in CUDA
On-chip programmable cache
Visible to threads in a block
Small, 16-48kB
High bandwidth
Low latency
CUDA C Programming Guide, NVIDIA Co.

## Slide 12: Now let’s try it!